## Slide 1
Subway Station Real-time Indoor Positioning System for Cell Phones
Chengqi Ma1
Chenyang Wan1; Yuen Wun Chau1; Soong Moon Kang2; David R. Selviah1;
1Department of Electronic & Electrical Engineering
2School of Management
University College London, UCL

## Slide 2
Server side: Tracking users’ cell phones. Collect data for study of users’ trajectories and monitoring congestion.
Client side: Navigation services in GPS-denied environments.
Functions
Server
Clients(real time)
Introduction

## Slide 3
Wi-Fi Fingerprinting
Localization Technologies:
Pedestrian Dead-Reckoning (PDR)
A radio ‘fingerprint’ is the pattern of radio signal strength measurements that is observed at a given location.
It comprises a vector of signal identity information (e.g. Wi-Fi MAC addresses, or cellular Cell-IDs) and a corresponding vector of values of Received Signal Strength (RSS).
Kalman Filter
Signal processing Technology:
Introduction

## Slide 4
≈14m
1) Body block effect
This is an example of the RSS distribution on a straight platform received from one AP when the device holder walks back and forth ten times.
Problems and Challenges

## Slide 5
Unstable signal strength
Wi-Fi signal (space/time)
Sensor data from cellphone
Environment variation
Periodically arriving and departing metallic trains
Group of people during different time periods
Problems and Challenges
2) Environmental variation effect

## Slide 6
Database Establishment
1) Pedestrian Dead-reckoning (PDR) mapping support
Testing set number | 1 | 2 | 3
Actual steps | 100 | 100 | 100
Average measured steps | 97 | 98 | 103
Null steps | 3 | 2 | 4
Average accumulated error | 1.89 metres | 1.26 metres | 1.89 metres
Overall accuracy | 97.3% |  | 

## Slide 7
2) Unique RSS distributions probability density function (PDF) fingerprint
Database Establishment
RSS histogram distributions from one AP at different reference points.
3) Extra information
Probability of occurrence R
Direction coefficient D

## Slide 8
Database Establishment
4) Database Scale
Around 40 APs can be detected at one reference point
2382 reference points in two stations.
1104 detectable APs
Data collecting work through a whole month

## Slide 9
Online Matching Phase

## Slide 10
Online Matching Phase
1) MAC address matching

## Slide 11
Online Matching Phase
2) Feature Matching
is a single tracking data RSS detected from one AP
is the feature distribution of the AP at one reference point
Pr

## Slide 12
Online Matching Phase
3) Probability Mark Selection
k-nearest neighbours selection function
For each selected reference point, we define and calculate a Mark to evaluate the matching probability

## Slide 13
Online Matching Phase
4) Discrete Kalman Filter
Trajectory smoothing
Matching failed point prediction
The Kalman filter is a widely used signal processing technique for trajectory optimization. It is a two-step algorithm for linear systems to help improve the estimation of their next states. Based on a given system’s current state and a dynamic model of the target trajectory, it initially predicts the next state of the system. The next step combines the predicted value with the actual value, giving rise to a more accurate estimate of the next state.

## Slide 14
System performance in separated areas
Experiment area | Off- peak time |  | Peak time | 
 | Matching result | Filtered result | Matching result | Filtered result
Platform | 1.97 m | 1.50 m | 4.91 m | 2.62 m
Tunnel | 1.92 m | 1.72 m | 2.15 m | 1.79 m
Escalator up | 1.23 m | 1.23 m | 4.23 m | 3.55 m
Escalator down | 0.91 m | 1.18 m | 2.73 m | 2.66 m

## Slide 15
System performance overall
System performance | Off- peak time |  | Peak time | 
 | Matching result | Filtered result | Matching result | Filtered result
Overall average error distance | 2.37 m | 1.71 m | 3.42 m | 2.90 m
80% CDF error distance | < 2.91 m | < 2.54 m | <4.77 m | <4.2 m

## Slide 16
Acknowledgements
The authors wish to thank the subway station operators for allowing us to carry out the experiments reported in this paper
Thank to my supervisor Dr David Selviah. Also thank to Dr Soong Moon Kang to provide this research opportunity.
Thank you all for listening !